## Slide 1: NPAC Performance Discussion
Presented to the LNPA-WG 3/8/2000

## Slide 2: Current Discussion Topics
Invalid CMIP Departure Times on SP requests to the NPAC resulting in association aborts
Effect of 1 x 15 retry timer change
Overall NPAC system performance during large volume porting scenarios
  Taking actual porting events as well as non-porting events into account

## Slide 3: Reasons for Invalid Departure Time Failures
There may be an attempt to violate system security
The systems clocks may not be synchronized
The sending system may queue the request for longer than 5 minutes due to system load
The NPAC system may queue the request for longer than 5 minutes due to system load

## Slide 4: Invalid Departure Time Failures (cont)
During heavy volumes the TCP/IP queue backs up and the departure time expires before the NPAC can service the request
There are several factors that may cause the NPAC to be unable to service the request
  Service provider queries
  Recovery mode processing from aborts
    Invalid departure time
    3x5 retry timeouts
    Provider aborts
  SOA message queuing
  Duplicate service provider requests, resulting in greater system load

## Slide 5: Effects of 1 x 15 Retry Timer
Current experience is limited (< 1 month)
Some reports have suggested that at least 1 retry, i.e. 2 x 8, might be more effective
Discussion ?

## Slide 6: NPAC Transaction Mix
Past observation of NPAC logs, etc. have suggested that an unexpectedly large volume of “non-porting” requests are being sent to the NPAC
These include:
  Mass Change requests
  Individual and Range TN query requests
  Large numbers of resync-network-data and resync-sv-data requests (from reassociation requests)

## Slide 7: Improvement Strategies
Cmip Departure time failures:
  Trial with one SP with timeout set to 20 minutes is underway
  Evaluate results of that trial in 30 days
  NeuStar will perform additional monitoring and reporting
1 x 15 Retry Timer
  Consider 2 x ?
Transaction Mix
  NeuStar will perform additional monitoring and reporting
  Guidelines and/or recommendations will be developed after additional data is obtained

## Slide 8: Improvement Timelines
NeuStar will provide updated reports to (LNPA-WG?) every 2-4 weeks
Next report update will include:
  Additional data from any invalid departure time occurrences
  Additional transaction mix data
  Association restart data